## Slide 1
16-Source Interrupt Controller
Priority Resolution, Selective Masking & Multi-Cycle Handshake Architecture
Team: T028 | 4 Students | Focus: Hardware Synchronization & Race Mitigation
M Abhiram Manikanta Reddy – 2400040026
B Lokesh – 2400040120
N Shashi Kiran Reddy – 2400040132
A Charan Teja Reddy – 2400040133

## Slide 2: Problem Statement

## Slide 3
16-Channel Line Aggregation
Combines 16 distinct peripheral hardware interrupt lines (IRQ0 to IRQ15) into a single processor interrupt request signal.
Translates pending hardware requests into a 4-bit vector ID during the CPU acknowledge pulse to streamline processing.
Preemptive Priority Handling
Supports nested interrupt priority rules, allowing critical high-priority events to interrupt running lower-priority handlers.
Provides software-configurable Interrupt Mask Registers (IMR) to selectively enable or suppress individual IRQ lines.
System Requirements & Use Cases

## Slide 4
16-bit Interrupt Request Register (IRR): Latches asynchronous peripheral inputs (IRQ0–IRQ15).
16-bit Interrupt Mask Register (IMR): Bitwise mask to disable or clear specific interrupt channels.
16-bit In-Service Register (ISR): Tracks currently executing interrupt levels for nested preemption.
Priority Resolver (PR): Combinational logic evaluating highest pending unmasked bit in real time.
16-Channel Architecture & Registers

## Slide 5
Nested Priority Handling
Nested Interrupt Handling
A higher-priority interrupt can preempt a currently active lower-priority interrupt. After the higher-priority interrupt is serviced, the processor can return to the lower-priority interrupt.
Fixed Priority Mode
IRQ15 holds the highest priority; IRQ0 holds the lowest priority. The priority resolver selects the highest-priority pending and unmasked interrupt.

## Slide 6
Block Diagram

## Slide 7
INTA Handshake Races
Race conditions occur when a new, higher-priority IRQ arrives in the middle of a multi-cycle CPU interrupt acknowledge handshake.
Level vs. Edge Triggering
Inconsistent pulse widths cause double interrupts (edge) or missing clears leading to endless IRQ re-triggering (level).
Pending Interrupt Management
New interrupts arriving while another interrupt is being acknowledged must be captured correctly and must not be lost. The pending register preserves unserviced interrupt requests for the next arbitration cycle.
Primary Hardware Bottlenecks

## Slide 8
Feature | Level-Triggered Mode | Edge-Triggered Mode
Detection Criterion | Active HIGH voltage level sustained on IRQ line | LOW-to-HIGH rising edge transition on IRQ line
Latching Mechanism | Remains pending while interrupt source is active | Latched when a rising edge is detected
Clearing Action | Source should deassert to prevent re-triggering | Pending interrupt is cleared when the interrupt is acknowledged.
Design Risk / Bottleneck | Stuck-at-HIGH pins cause repeated interrupt servicing | Glitch sensitivity; lost pulses if pulse width < t_CLK
Level vs. Edge Trigger Analysis

## Slide 9
1. IRQ Arrival
Peripheral asserts IRQ; unmasked line latches into IRR.
2. Priority Lock
Priority resolver freezes winner to prevent mid-cycle races.
3. INTA Cycle 1
CPU acknowledges; latched vector ID locked into output buffer.
4. INTA Cycle 2
Vector sent to data bus; winner bit moved to ISR register.
INTA Handshake & Race Control

## Slide 10
16:1
Peripheral IRQ Aggregation Ratio
Resolving Handshake Races
By implementing a 2-stage synchronizer and an atomic Priority Freeze Latch on INTA assert, Team T028 resolves race conditions cleanly.
New incoming IRQs during an active INTA cycle are queued safely in the IRR for the next arbitration cycle without corrupting the active vector bus.
16-Line Vector Aggregation

## Slide 11
Vivado schematic

## Slide 12: Cadence Synthesis

## Slide 13: Result Vivado:

## Slide 14
Cadence Result

## Slide 15: Design Rule Check

## Slide 16: Power Analysis

## Slide 17: Filter

## Slide 18: Verify Connectivity

## Slide 19: GDSII

## Slide 20: Verification

## Slide 26: Thank you